## Slide 1: Security Issues Related to Pentium System Management Mode
Loïc Duflot
Direction Centrale de la Sécurité des Systèmes d’Information
loic.duflot@sgdn.pm.gouv.fr
SGDN/DCSSI 51 boulevard de la Tour Maubourg 75007 Paris

## Slide 2: Outline
Introduction
PC architecture and I/O access
Using System Management Mode to Circumvent Operating System Security
A sample exploit on OpenBSD systems
Conclusions

## Slide 3: Introduction
Pentium System Management mode can be used to circumvent operating system security mechanisms.
An example of how hardware functionalities can be misused by an attacker as a means for privilege escalation.
Only legal and documented functionalities are used in the privilege escalation scheme.
A generic approach…: Pentium®, P6 (Pentium® IV, Xeon®), Pentium® clones.
… whenever the functionality exists. (some chipset do not implement SMM-related functionalities)

## Slide 4: Outline
Introduction
PC architecture and I/O access
Using System Management Mode to Circumvent Operating System Security
A sample exploit on OpenBSD systems
Conclusions

## Slide 5: Simplified Pentium 4 architecture
Ethernet
USB
IDE
LPC
PCI
Hub Link
Front Side Bus
RAM
Display
Adapter
Processor
North-
Bridge
Southbridge
Chipset

## Slide 6: I/O ports access
I/O access mechanisms:
  Memory mapped I/O (MMIO)
      I/O registers are mapped in physical address space.
  Programmed I/O (PIO)
      I/O registers are mapped on a separate 16-bit bus.
  Direct Memory Access (DMA)
      Peripherals act as masters on the PCI bus.
IRQ to the processor.
      Unidirectional.
      Asynchronous.

## Slide 7: Four modes of operation
Protected Mode
Virtual 8086 Mode
Real Address Mode
System Management
Mode
SMI
rsm
PE=0 or reset
PE=1
VM=0 or Int.
VM=1
reset
SMI
SMI
rsm
rsm or reset

## Slide 8: Protected mode
Hardware security mechanisms:
  Privilege rings:
    Most privileged: Ring 0 (kernel execution)
    Least privileged: Ring 3 (user space code)
  Segmentation and Paging.
Hardware-based memory protection checks.
Restricted instructions (HLT, LGDT, INVD).
Mode of execution of most operating systems (Windows, Linux, OpenBSD…)

## Slide 9: Protecting memory: Hardware mechanisms
Segmentation:
  Privilege rings
  Segment access restrictions (type and DPL)
Paging (when enabled):
  User/supervisor bit
  Read/Write bit
  No eXecute/ eXecute Disable bit
Quite a few security techniques (W^X, PaX…) rely upon such mechanisms.

## Slide 10: Programmed I/O access
Two different hardware mechanisms:
  Set IOPL bits. (EFLAGS register)
  Clear bits in the I/O bitmap of the current hardware task.
-> Two different system calls:
  iopl (i386_iopl, /dev/io and the like)
  ioperm (i386_set_ioperm and the like)

## Slide 11: System Management mode
Maintenance mode:
  Used for efficient power management.
  Run specific proprietary code.
SMI
SMI
SMI
SMI
RSM instruction
SMM
Back to calling context
Assert a “System Management Interrupt” (SMI) from any other mode:
Thermal Sensor
Century Rollover
RTC Alarm
TCO, USB

## Slide 12: Generating the SMI

## Slide 13: System Management mode
A separate execution space:
  Every processor register is saved upon assertion of the SMI.
  The context (state) will be restored upon execution of « RSM ».
In SMM:
  Free access to all physical memory.
  Free access to all Programmed I/O ports.

## Slide 14: Memory in SMM
16-bit mode.
All 4 Gb of physical memory may be accessed.
Real mode addressing style. (20-bit)
But: segment limits are extended to 4 Gb.
And: 32-bit operand-size override prefixes may be used.

## Slide 15: Real Address mode
16-bit mode: 1 Mb address space
Address Translation:
  Segment:Offset = Segment <<4 + Offset
  Example: 0xA000:0x8000 = 0xA8000
Mostly used:
  At startup and shutdown time.
  May be used to benefit from BIOS functionalities.
Transitions to protected mode unrestricted. Transitions from protected mode restricted.
A 8086 processor just a little faster!

## Slide 16: Virtual 8086 mode
Virtual mode embedded into protected mode.
Ring 3 execution context.
Simulate the behavior of a 8086 processor.
Paging may be used.
16-bit mode.
Access is only allowed during hardware task switch or interrupt handling.

## Slide 17: Memory Protection
So Paging and Segmentation security mechanisms only exist in Protected Mode.
“PaX/Segmexec prevent introduction/execution of arbitrary code”.
Well that’s not true outside of protected mode!!!
But that’s ok because there is no way to switch to other modes from userspace, right?

## Slide 18: Outline
Introduction
PC architecture and I/O access
Using System Management Mode to Circumvent Operating System Security
A sample exploit on OpenBSD systems
Conclusions

## Slide 19: SMRAM
SMBASE + 0xFFFF
SMBASE + 0xFE00
SMBASE +0x8000
SMBASE
SMRAM
First SMI Handler instruction
Processor context prior SMI
assertion
Code, Heap and Stack
State save area
Physically localized in unused memory blocks
SMBASE + 0x1FFFF
Usually SMBASE=0xA0000
Intel processor doc: SMBASE=0x30000
Intel Chipset doc: SMBASE=0xA0000

## Slide 20: State Save Area Map
Instruction pointer
IOPL bits
Code segment
Task register
Stack pointer

## Slide 21: Accessing SMRAM
Access to physical address 0xA8000
Protected Mode
if D_OPEN = 1
if D_OPEN = 0
SMM Mode
Ethernet
USB
IDE
LPC
PCI
Hub Link
RAM
(including SMRAM)
Display
Adapter
Processor
North-
Bridge
Southbridge

## Slide 22: SMRAM control register
D_CLOSE
D_OPEN
D_LCK
Enable
Reserved
7
0
Chipset-specific
SMRAM control register:
8-bit register
D_LCK: Locks SMRAM control register.
D_OPEN: Enables all SMRAM accesses even if not in SMM.
D_CLOSE: No data type accesses to SMRAM space.
Enable: Enables SMM functionalities
Read-Only

## Slide 23: Possible attack scheme
Enable System Management Interrupts.
Open SMRAM space.
Replace default SMI Handler by custom one.
Close SMRAM space.
Trigger SMI.
Gain access to restricted operations.

## Slide 24: Required privileges
I/O access privileges on the SMRAM control register.
I/O access privileges on at least one of the I/O registers that can trigger the SMI.
Optional I/O access to corresponding SMI-enable registers.
Write access to SMRAM (0xA0000-BFFFFF)
  -> Write access to the legacy video RAM.

## Slide 25: Outline
Introduction
PC architecture and I/O access
Using System Management Mode to Circumvent Operating System Security
A sample exploit on OpenBSD systems
Conclusions

## Slide 26: OpenBSD
Security-aware operating system.
Proactive security.
Memory protection: W^X, guard pages, randomized malloc() and mmap(), etc...
Secure levels.

## Slide 27: OpenBSD
The Secure Levels:

## Slide 28: Physical Memory Access
On OpenBSD-based systems:
  If securelevel >0 /dev/mem and /dev/kmem cannot be written to.
  This means that even root cannot directly write to physical memory.
  And yet, the display server (X) needs to be able to map MMIO devices.

## Slide 29: /dev/xf86
Use of the /dev/xf86 pseudo-file.
/dev/mem but only in video memory areas.
May be opened at most once (at a time).
Cannot be opened if the machdep.allowaperture variable is set to 0.

## Slide 30: Allowaperture
If set access to /dev/xf86 is allowed.
Otherwise prevents access to both /dev/xf86 and i386_iopl() (and i386_set_ioperm).

## Slide 31: Programmed I/O ports access
On OpenBSD two different system calls are available:
  i386_iopl
  i386_set_ioperm
  + Linux (linux_sys_iopl, linux_sys_ioperm) and FreeBSD (KDENABIO ioctl) compatibility system calls.
But i386_set_ioperm cannot be used to request access to ports 0xcfc and 0xcf8.
i386_iopl and i386_set_ioperm restricted to superuser-owned processes.

## Slide 32: A sample exploit against OpenBSD
We assume that the target system is running OpenBSD in Highly Secure mode with allowaperture=1.
We assume that an attacker has found a way to execute code with superuser privileges.
Thus, the attacker may use the i386_iopl call (unrestricted Programmed I/O access) and write to the /dev/xf86 device (write access to the 0xA0000-0xBFFFF memory range).
But the attacker still lacks a way to get to kernel (ring 0 random code execution) privileges…

## Slide 33: Sample proof-of-concept exploit
A root in highly secure mode (or secure level) to kernel privilege escalation scheme.
Aim: For example, lower the securelevel to « Permanently insecure ».
Bonus: Modification of the EIP register while in SMM.
Experimentations carried out on a PC equipped with a Pentium® 4, and a Intel® MCH/GMCH-ICH2/ICH5 chipset.

## Slide 34: 1st step: Locating the securelevel variable
Virtual address: nm /bsd | grep securelevel.
Physical Address:
Virtual memory space
Physical memory space
Kernel
Kernel
0
0
4Go
4Go
0xd0000000 offset
Example on OpenBSD 3.5

## Slide 35: 2nd Step: Craft Handler

## Slide 36: 3rd Step: Default Handler Replacement

## Slide 37: Last step: SMI generation

## Slide 38: Did it work?
Return to protected mode overwrites EIP with the address of the test function.
The program displays that the secure level has been lowered. This proves that we had successfully gone into SMM.
Check that the secure level was lowered.

## Slide 39: Possible countermeasures
Decision from the system administrator: decide that the X server will not be used.
  machdep.allowaperture = 0
Patch the BIOS or the OS: Set the D_LCK bit in the early boot stages.
Prevent access to the SMRAM register:
  Programmed I/O filter.
  No IOPL, I/O Bitmap management only.
No PIO accesses from ring 3 code.

## Slide 40: Outline
Introduction
PC architecture and I/O access
Using System Management Mode to Circumvent Operating System Security
A sample exploit on OpenBSD systems
Conclusions

## Slide 41: Efficiency of the attack
Systems | Attack scheme works
Windows XP | 
Linux 2.6 | 
FreeBSD | 
NetBSD | 
OpenBSD | 

## Slide 42: Privilege escalation
On most systems, being able to carry out this scheme means being granted superuser privileges.
On OpenBSD, root is only granted limited privileges. That is why the attack scheme is effective.
There may be easier ways to bypass the Secure Level mechanism. But more than the result, the attack scheme in itself is interesting: unused, legacy or routinely used functionalities can be used from userspace to circumvent operating system security functions.
One of the problems is X requiring too many privileges.
Notes: Can X be tricked into modifying SMRAM code?

## Slide 43: Conclusion
Only documented functionalities of the Pentium® processor and its chipset were used…
… and yet we have been able to circumvent operating system security functions.
Would this point to a consistency issue in hardware and OS security models?
  IOPL and I/O privileges at stake.
This demonstrates the need for trust in, and wise use of, hardware components.

## Slide 44: Any questions?
Thank you!
loic.duflot@sgdn.pm.gouv.fr
Joint work with: Olivier Grumelard (SGDN/DCSSI)
Daniel Etiemble (Paris XI University, LRI)